## Slide 1: Using unmanned aircraft to provide near real-time updates of biomass, forest structure and land use in the Western Amazon
A new look at an old problem
Max Messinger

## Slide 2
Notes: 40,000 from 195
Forest conservation is a big part
Now we have to figure out how to turn words into actions

## Slide 3
Notes: In addition to carbon, there is extreme biodiversity (this is vertebrates)
Over 1,000 bird sp, 10,000 trees

## Slide 4
University of Maryland
Notes: Deforestation is expanding, accelerating in Amazon
Still a lot of forest left in the Amazon, biggest tropical wilderness on Earth
What you really have a hard time seeing here is the extensive fragmentation that goes on

## Slide 5
Finer and Novoa 2015
Notes: So now Peru, where we see that fragmentation
This is CLASlite
All color is deforestation
But we don’t know the cause

## Slide 6
Notes: Governance is another issue
Size of SC
Much protected area, much reserved for responsible land use
Timber, agriculture, reforestation, agroforestry, tourism
Wild East
Peru is having a very hard time governing this space with their limited resources

## Slide 7: The Problem
Massive forest loss from gold mining and other drivers
Fine-scale activity makes monitoring with space-borne sensors difficult
CLASlite provides deforestation detection but provides no information about cause
Manned aircraft are too expensive for frequent monitoring
Notes: *** Reforestation is critical*** We often focus on deforestation but these mines are typically abandoned after only a few years of activity

## Slide 8: Goals
Carbon conservation and management
  Develop an effective method for frequent and accurate forest carbon estimation in a variety of forest types
  Develop an integrated system to rapidly detect forest disturbance, quantify its impacts, and conduct long-term monitoring

## Slide 9
Notes: Current state of the art, amazing tool, tens of millions of $$

## Slide 10: Deacon Airborne Observatory
Notes: Our answer
Fully autonomous
Comparatively fast, long range, able to cover a lot of ground (250 ha/flight)

## Slide 11: The Process
Collect Imagery
Structure-from-Motion
Create Canopy Model
Calculate Canopy-Height
Model Aboveground Carbon

## Slide 14
250
360

## Slide 15
250
305

## Slide 16
0
55

## Slide 18
Canopy Height (m)
Aboveground Carbon (Mg C ha-1)
Asner and Mascaro 2014

## Slide 19: Aboveground Carbon Model
 | Aboveground carbon
 | Canopy height
 | Regional mean basal area
 | Basal-area weighted wood density
, , , | Coefficients (Estimated by Asner and Mascaro 2014)
 | Aboveground carbon
 | Canopy height
 | Regional mean basal area
 | Basal-area weighted wood density
 | Coefficients (Estimated by Asner and Mascaro 2014)

## Slide 21: Goals
Carbon conservation and management
  Develop an effective method for frequent and accurate forest carbon estimation in a variety of forest types
  Develop an integrated system to rapidly detect forest disturbance, quantify its impacts, and conduct long-term monitoring

## Slide 22
Notes: And we got a lot of imagery like this.
Here is a scene with old mining at the bottom (you can see vegetation growing on the tailing piles) and
***inside this circle we see current mining

## Slide 23
Notes: But we also got stuff like this, a newly cleared field by a small settlement. Differentiating between these is important, as while they are both deforestation they have very different impacts on the environment.
We are working to integrate the aircraft into the routine monitoring framework in this area by building local capacity to operate them

## Slide 24: Long-Term Forest Monitoring
Carbon baseline
Estimate of lost carbon
Database of disturbance
Estimation of forest recover and carbon accumulation through time

## Slide 25
Notes: This is our newest aircraft, a gas powered, 3m wingspan plane which will hopefully provide us 5 hours of flight time at 120km/h and the ability to carry much heavier payloads, i.e. LIDAR, hyperspec, etc

## Slide 26: Going to Scale
Data Challenges:
  Storage: ~200 GB/day generation, 4 days/week operation, ~40 TB/year
  Processing: Demand will be ~10-15 TFLOPS
  Distribution: Need to deliver data products in near real-time
The Kicker:
  Intermittent power availability
  Low-bandwidth and intermittent networking

## Slide 27: Conclusions
Better information about carbon cycling, especially in novel disturbance regimes
High-frequency updates about the location, size, and nature of forest disturbance
Better informed governance
Low cost forest carbon monitoring for the forestry and payment-for-ecosystem-services market

## Slide 28: Conclusions
Future directions:
  Integrate into existing conservation, governance, and commercial forest monitoring networks
  Develop a better understanding of the behavior of post-mining succession
  Determine usability of space-borne RADAR (SRTM) as a replacement for LIDAR terrain model
  Determine usability of space-borne RADAR (i.e. PALSAR-2) for forest disturbance detection
  Streamlining/automating workflows

## Slide 29: Made possible by:
The Sabin Family Foundation
The Winston-Salem Foundation

## Slide 30: Acknowledgments
Advisor: Miles Silman
Committee: Bill Smith
Michael Anderson
Paul Pauca
Team SUAS: Marcus Wright
Tim King
Billy Nicholson
Nella Hendley
Matt Gray
Team ACCA: Carlos Castañeda
Carlos Quispe
Silman Lab: Rachel Hillyer
William Farfan
Noah Yavit
Karina Garcia
Collaborators: Greg Asner and lab
Matt Finer
Sidney Novoa

## Slide 31
Questions?
max@linnaero.com